## Slide 1: Deploying IP Anycast
Kevin Miller
Carnegie Mellon Network Group
kcm@cmu.edu
NANOG 29 – October 2003

## Slide 2: Overview
Why anycast?
  Server load balancing
  Service reliability
  Client transparency
  Locality / latency improvements
  Distributed response to DoS
Assume experience with unicast routing
http://www.net.cmu.edu/pres/anycast
Notes: Several compelling reasons for the use of anycast
Assume unicast experience; anycast requires no changes to clients, and very minimal server changes
Simply exploiting existing IP / IP routing functionality

## Slide 3: Agenda
What is Anycast?
Deploying IPv4 anycast services
Anycast usage case studies
Advanced Topics

## Slide 4: Not Unicast
Unicast: Single host receives all traffic
Notes: Abstract diagram; considering all links equal cost
Traffic from node 2.2 to node 7.1

## Slide 5: Not Multicast
Multicast: Many hosts receive (all) traffic to multicast group
Notes: Multicast group address: 233.0.9.3
Nodes 1.2, 3.1, 5.3 all subscribe to multicast stream
Node 2.2 sending to multicast group address

## Slide 6: Anycast
Multiple nodes configured to accept traffic on single IP address
Usually, one node receives each packet
  Packet could be dropped like any other
  Preferably only one node receives packet, but no absolute guarantee
The node that receives a specific packet is determined by routing.
Notes: Vast majority of the time, only one node gets the packet. (That’s really the whole point.)

## Slide 7: Anycast
Three nodes configured with anycast address (10.5.0.1)
Notes: Anycast address: 10.5.0.1

## Slide 8: Anycast
Potentially equal-cost multi-path

## Slide 9: Anycast
Sequential packets may be delivered to different anycast nodes
Notes: Three sequential packets (labelled 1, 2, 3) follow different paths
FLOW CACHING

## Slide 10: Anycast
Traffic from different nodes may follow separate paths

## Slide 11: Anycast
Server receiving a packet is determined by unicast routing
Sequential packets from a client to an anycast address may be delivered to different servers
Best used for single request/response type protocols

## Slide 12: Anycast
Clients, servers, and routers require no special software/firmware
Does not negatively interfere with existing networks
Just leveraging existing infrastructure

## Slide 13: Anycast Documented
Concept discussed in RFC1546 (11/93)
  Current practices have evolved from operational experience
  CIDR eliminated a hurdle from 1546
Evolution is briefly documented in RFC2101 (2/97)
Anycast DNS noted in RFC2181 (7/97)
  Reply source address must match request dest address
Notes: 2101: LOCATOR VS IDENTIFIER: anycast is one of many things reducing the usefulness of IP addresses as identifiers. Instead it’s a locator only
2181: source address of DNS response must come from the dest address of the request, unless the address is not legal on the node..

## Slide 14: Anycast Documented
IPv6 anycast – different, will discuss later
  Architecture (RFC1884, now RFC3513)
  Reserved anycast addresses (RFC2526)
  Anycast v4 prefix for 6to4 routers (RFC3068)
  Source address selection (RFC3484)
  DHCP (RFC3315)
Anycast authoritative name service (RFC3258)
Anycast for multicast RP (RFC3446)
ISC Technote (ISC-TN-2003-1)
Term ‘anycast’ used in 51 RFCs total
Notes: 1884/3513, 2526: will discuss in more detail later
51 RFCs through RFC3627

## Slide 15: Agenda
Deploying IPv4 anycast services
  Address selection
  Host configuration
  Service configuration
  Network configuration
  Monitoring and using anycasted service

## Slide 16: Address Selection
Current practice is to assign anycast addresses from unicast IP space
Designate small subnet(s) for anycast use
  Consider best practices of inter-domain routing announcements
  /24 is a popular selection
  Subnet may not be attached to any interface
Notes: Best practices:
- Ideally, don’t announce pieces of larger allocations
- Some filtering occurs on very short prefixes
F root server: 192.5.5.0/24
AS112: 192.175.48.6/24
.ORG: 204.74.112.0/24, 204.74.113.0/24

## Slide 17: Host Configuration
Hosts need to be configured to accept traffic to anycast address
Want to maintain a unique management address on each host
Typically, anycast addresses are configured as additional loopbacks
Make sure ingress filters are updated!

## Slide 18: Configuring Addresses
# ifconfig lo:1 10.5.0.1 netmask 255.255.255.255 up
# ifconfig lo:1
lo:1 Link encap:Local Loopback
inet addr:10.5.0.1 Mask:255.255.255.255
UP LOOPBACK RUNNING MTU:16436 Metric:1
Linux
# ifconfig lo0 alias 10.5.0.1 netmask 255.255.255.255
# ifconfig lo0
lo0: flags=8049<UP,LOOPBACK,RUNNING,MULTICAST> mtu 33224
inet 127.0.0.1 netmask 0xff000000
inet 10.5.0.1 netmask 0xffffffff
OpenBSD
Notes: OSs have different methods for configuring additional loopback addresses/aliases

## Slide 19: Configuring Addresses
# ifconfig lo0 addif 10.5.0.1/32 up
Created new logical interface lo0:1
# ifconfig lo0:1
lo0:1: flags=1000849<UP,LOOPBACK,RUNNING,MULTICAST,IPv4>
inet 10.5.0.1 netmask ffffffff
Solaris

## Slide 20: Network Configuration
Correctly configuring the network may be the trickiest aspect of anycast
Intra-domain vs. inter-domain configuration
Notes: Intra-domain vs. inter-domain: we’ll address both, and both need to be considered

## Slide 21: Intra-Domain Configuration
If the anycasted service is entirely within your routing domain, only intra-domain consideration is needed
  All anycast nodes are within domain
  Or multiple “intra-domain” locations
Need to configure routing to deliver anycast traffic to servers
Notes: Entirely within routing domain == all anycast nodes are completely within domain

## Slide 22: Static IGP Routes
Simple: configure static routes on first-hop routers (host routes)
Ensure routes are propagated through domain
Notes: In this diagram, “C”, “E”, and “G” would have static routes to 10.5.0.1 via the unique IP address of the server

## Slide 23: Static IGP Routes
Simple to configure
Doesn’t respond quickly to server failure
Provides the ability to relocate servers without service outage, though

## Slide 24: Dynamic IGP Routes
Run a host-based routing daemon on anycast servers
  GateD
  Zebra/Quagga
Host itself is route originator
When host is down, route is withdrawn
Leverages routing infrastructure
Notes: Route is withdrawn by upstream routers when they lose adjacency
Zebra: www.zebra.org
Quagga (zebra descendant): www.quagga.net
Leveraging routing infrastructure: that’s what anycast is: leveraging existing technology

## Slide 25: Dynamic IGP Routes
Each host announces route to IGP cloud

## Slide 26: Dynamic IGP Routes
Configuration obviously specific to IGP
  Connected route redistribution, if anycast addresses are host loopbacks
Host up doesn’t imply service is up
  Want a mechanism for withdrawing routes automatically when service is unusable

## Slide 27: Inter-Domain Configuration
Follow traditional BGP operating rules
  Announce from a consistent origin AS
  Advertise the service/anycast supernet
  Limit route flapping
  Provider-independent IP space

## Slide 28: Inter-Domain Configuration
Intra-domain routing must be correct
  Servers can be iBGP peered; ‘network’ style announcement on the host
  Can use IGP with redistribution
Withdraw routes when service is unavailable at a particular location

## Slide 29: Inter-Domain Configuration
Some deployments distinguish “global” nodes from “local” nodes
  Global nodes are announced without limitation; upstream provides transit
  Local nodes add “no-export” community to limit the clients that will use the node
Why?
  Money (global/local imply different relationships)
  Node stability, capabilities (due to service area)
Notes: Local nodes don’t need to be as capable as global nodes, nor as stable. If they need to be taken offline for a few days, that’s ok (because a global node will provide service). But global nodes must always be available.

## Slide 30: Inter-Domain Configuration
AS65501
Transit
Global 1
10.5.0.1/24
AS65500
Local 1
10.5.0.1/24
AS65500
AS65505
End Site
AS65530
NoExport Peer
AS65515
End Site
AS65520
NoExport
AS65510
Transit Peer
AS65535
End Site
AS65525
End Site
Notes: Direct customers of AS65520, the no-export peer to a local node, will most likely use the local node.
However, AS65530 is a peer of 65520, so it would not receive the no-export route. Thus, AS65535
will use the global node instead of the local node.

## Slide 31: Service Configuration
Obviously depends on implementation
Configure service to listen on anycast IP
  Most require no special configuration
  Verify that service responds from anycast address when queried
  May want to limit service to listen only on anycast IP address
Assume: identical service by each server
Notes: Some services don’t work correctly with anycast: for example ‘time’ / UDP from inetd on RedHat
Limit to anycast address: makes it easier to relocate service

## Slide 32: Anycast Address Use
Clients told to use anycast addresses
Anycast service configured by name
  Authoritative DNS, Syslog, Kerberos
  Can use round-robin DNS for additional redundancy
;; ANSWER SECTION:
ns1.example.com. 86400 IN A 10.5.0.1

## Slide 33: Anycast Address Use
Caching DNS Service
  Assign server addresses by DHCP, PPP, word of mouth
  Note the poor behavior of OS stub resolvers
    The first configured DNS Server is tried on every query
    Results in multi-second delays for many queries
    Perfect opportunity for anycast
Notes: See LISA presentation for more insights on recursive resolver behavior.

## Slide 34: Monitoring
Monitoring is more complicated
Could monitor the unique (non-anycast) IPs, but doesn’t verify the actual service
Monitoring the anycast (service) IP can’t be done centrally
Distributed monitoring needed for distributed service
Also want to monitor routes
Notes: EXTRA SLIDE: IDENTIFYING SPECIFIC NODE

## Slide 35: Agenda
What is Anycast?
Deploying IPv4 anycast services
Anycast usage case studies
Advanced Topics

## Slide 36: Anycast in Action
Authoritative DNS
  AS 112
  Root Servers: F, I, K, others
  .ORG Top Level Domain
Caching DNS
Anycast for Multicast RP
Anycast Sink Holes
6to4 routers (RFC3068)
Notes: http://root-servers.org

## Slide 37: AS112 Project
Problem: Many clients try queries and updates for/to RFC1918/link local reverse zones
Goal: Reduce unnecessary root server load from these queries/updates
Solution: Delegate reverse zones to anycasted black-hole servers.
www.as112.net
Notes: DO NOT SEOCNDARY AS112 UNLESS YOU TALK TO THEM
http://www.as112.net
192.175.48.1 – SOA RR listed
192.175.48.6 – NS record
192.175.48.42 – NS record

## Slide 38: AS112 Project
Black-hole servers use IPs in 192.175.48.0/24
Announced from 16 locations worldwide
Common origin AS112
Notes: As of September 19, 2003
http://www.chagreslabs.net/jmbrown/research/as112/

## Slide 39: Configuring BGP
router bgp 112 bgp router-id 192.175.48.254 network 192.175.48.0 neighbor PEER_IP remote-as PEER_AS neighbor PEER_IP ebgp-multihop neighbor PEER_IP next-hop-self
One Vendor..
policy-statement advertise-aggregate {
term first-term {
from protocol aggregate;
then accept;
}
term second-term {
from route-filter 192.175.48.0/24 longer;
then reject;
}
}
[continued]
Another Vendor..
[http://www.chagreslabs.net/jmbrown/research/as112/]

## Slide 40: Configuring BGP
# set routing-options aggregate route 192.175.48.0/24
[edit protocols bgp group 112]
# set export advertise-aggregate
# set type external
# set peer-as PEER_AS
# set neighbor PEER_IP
Another Vendor..

## Slide 41: AS112 Project
zone “10.in-addr.arpa” { type master; file “db.RFC-1918”; };
zone “254.169.in-addr.arpa” { type master; file “db.RFC-1918”; };
...
BIND Configuration
$TTL 300 @ IN SOA prisoner.iana.org. hostmaster.root-servers.org. ( 2002040800 30m 15m 1w 1w ) NS blackhole-1.iana.org. NS blackhole-2.iana.org.
Zone File: db.RFC-1918
[http://www.chagreslabs.net/jmbrown/research/as112/]

## Slide 42: Root Servers
Problems:
  Low concentration of root servers outside the US (high latency, higher cost links)
  DoS attacks hurt the root servers and infrastructure in between
  Can’t just add more NS records to root zone
Goal: Add root servers to underrepresented areas of the world
Solution: Use inter-domain anycast to serve existing root server IP addresses
Notes: Problems: high latency to root server.. More time to get DNS responses back.
Can’t add more NS records: size of DNS responses is bounded, and want to fit servers + glue in one packet

## Slide 43: Root Servers
“F” root server (ISC) anycasted
  First cloned node announced Nov. 2002
  Now have 12 locations
  Common origin AS3557
  Second hop AS for local nodes also assigned to the ISC
... 3557 3557 3557
Global Node AS Path
... 23709 3557
Local Node AS Path (Ex)
Notes: http://f.root-servers.org, as of 18 sept 03

## Slide 44: .ORG Top Level Domain
Recent NANOG discussion analyzing anycast use for .ORG
Suggestion of an outage at one location
  “the monitors that test each of the anycast nodes reported no outages”
DNS provided by 2 anycast servers (204.74.112.1, 204.74.113.1)
Two /24s; different transit providers
Eleven total second-hop ASs
Notes: Beginning of “.ORG problems this evening”: http://www.merit.edu/mail.archives/nanog/2003-09/msg00741.html
Note from Rodney Joffe to NANOG list 9/17/2003
http://www.merit.edu/mail.archives/nanog/2003-09/msg00748.html
DNS servers: 204.74.112.1, 204.74.113.1
Origin AS: 12008
From route-views.oregon-ix.net:
204.74.112.1:
2914: Verio (Transit)
8001: Net Access
19029: New Edge Networks
2516: KDDI Corporation
6079: RCN Corp
6939: Hurricane Electric
8075: Microsoft/MSN -- No Whois information??
12956: Telefonica
4513: Globix
4181: TDS Telecom
204.74.113.1:
12956: Telefonica
2828: XO Communications (Transit)
19029: New Edge Networks
2516: KDDI Corporation
8075: Microsoft/MSN
6939: Hurricane Electric

## Slide 45: .ORG Top Level Domain
Highlights anycast lessons
  Operators will encounter anycast
    Different locations, different experiences
  Service availability and routing announcements are coupled
  Consider reliability mechanisms built into service – they can help or hurt
Notes: Operators *will* encounter anycast in ordinary network operations. Have to be careful about assumptions made..
Route-views servers useful in determining global picture.. Perhaps “dns views” servers also useful?
Good deployments will make sure routing is withdrawn quickly when the service is unavailable.
Built-in reliability mechs: perhaps use multiple DNS servers in zone, have one IP NOT hosted at each POP
  Rodney doesn’t believe this is necessary or improves reliability.

## Slide 46: Caching DNS
Problems:
  Hosts respond poorly when caching nameserver is unreachable
  Caching NS is hard to re-IP (static configs)
Goal: Always have caching DNS service on first client-configured IP
Solution: Use anycasted servers; configure anycast IPs on clients
Notes: Typically intra-domain
Hard to re-ip given that clients refer to the IP explicitly; that’s the whole point

## Slide 47: Caching DNS
We designated 128.2.1.0/26 for intra-domain anycast use (from our IP space)
Two caching server IPs: 128.2.1.10, 128.2.1.11
Using BIND9
Configured on 4 servers; 6 interfaces
Addresses assigned by DHCP, PPP

## Slide 48: Caching DNS
Each server runs host-based routing daemon (Quagga) to join OSPF cloud
Using OSPF NSSA areas to hosts
  Minimizes the number of routes on the servers
  Enables multiple interfaces on servers in separate NSSA areas but no forwarding through server

## Slide 49: Caching DNS Config
options {
listen-on { 128.2.1.10; 128.2.1.11; };
query-source address 128.2.4.21;
};
BIND 9 Changes
router ospf 1
area 0.0.0.0 authentication message-digest
area 128.2.4.0 authentication message-digest
area 128.2.4.0 nssa default-information-originate no-summary
network 128.2.4.0 0.0.0.63 area 128.2.4.0
network 128.2.0.0 0.0.255.255 area 0.0.0.0
Upstream Router Changes

## Slide 50: Caching DNS Config
options {
listen-on { 128.2.1.10; 128.2.1.11; };
query-source address 128.2.4.21;
};
BIND 9 Changes
router ospf 1
area 0.0.0.0 authentication message-digest
area 128.2.4.0 authentication message-digest
area 128.2.4.0 nssa default-information-originate no-summary
network 128.2.4.0 0.0.0.63 area 128.2.4.0
network 128.2.0.0 0.0.255.255 area 0.0.0.0
Upstream Router Changes
Note generic lesson:
Make sure servers aren’t sourcing non-response traffic from anycast addresses.

## Slide 51: Caching DNS Config
[edit protocols ospf]
area 4 {
nssa {
area-range 128.2.4.0/26;
default-lsa {
default-metric metric;
type-7;
}
no-summaries;
}
authentication-type md5;
interface interface;
}
Upstream Router, Said Another Way

## Slide 52: Host-Based Router Config
interface eth0
ip address 128.2.4.21/26
!
interface lo:1
ip address 128.2.1.10/32
!
interface lo:2
ip address 128.2.1.11/32
quagga.conf
interface eth0
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 [key]
!
router ospf
ospf router-id 128.2.4.21
ospf abr-type cisco
compatible rfc1583
area 128.2.4.0 authentication message
area 128.2.4.0 nssa
network 128.2.4.21/26 area 128.2.4.0
redistribute connected
distribute-list 50 out connected
!
access-list 50 permit host 128.2.1.10
access-list 50 permit host 128.2.1.11
ospfd.conf

## Slide 53: Multicast RP
Problem:
  PIM-SM specifies one active RP per multicast group at a time
  A routing domain may be too large for this to be feasible (RP on the other coast)
  Slow failover if RP fails
  Not directly possible for shared-tree load balancing
Goal: Multiple RPs for same group within a routing domain
Solution: Use anycast addresses for RP (RFC3446)
Notes: RFC3446
Difficult to

## Slide 54: Multicast RP
Designate more than one RP
Assign anycast address as loopback on each RP
Configure all other routers to use anycast address as RP for all groups
Setup MSDP mesh among all RPs (using unique addresses)
  RP address cannot be used in SA messages

## Slide 55: Multicast RP
interface Loopback0
description Router Management
ip address 10.2.4.249 255.255.255.255
ip pim sparse-mode
interface Loopback1
description Anycast RP Interface
ip address 10.2.1.130 255.255.255.255
ip pim sparse-mode
!
ip msdp peer 10.2.4.248 connect-source Loopback0
ip msdp peer 10.2.4.250 connect-source Loopback0
ip msdp mesh-group CMU-MSDP 10.2.4.248
ip msdp mesh-group CMU-MSDP 10.2.4.250
ip msdp cache-sa-state
ip msdp originator-id Loopback0
RP Routers
ip pim rp-address 10.2.1.130 override
ip pim accept-rp 10.2.1.130
Non-RP Routers

## Slide 56: Multicast RP
[edit interfaces lo0 unit 0 family inet]
# set address 10.2.4.249/32
# set address 10.2.1.130/32
[edit protocols pim]
rp {
local {
address 10.2.1.130;
}
}
interface all {
mode sparse;
version 2;
}
[edit protocols msdp]
group CMU-MSDP {
local-address 10.2.4.249;
mode mesh-group;
peer 10.2.4.248;
peer 10.2.4.250;
}
RP Routers
[edit protocols pim]
rp {
static {
address 10.2.1.130 {
version 2;
}
}
}
Non-RP Routers
Notes: http://www.juniper.net/techpubs/software/junos/junos60/swconfig60-multicast/html/pim-config41.html

## Slide 57: Multicast RP
eBGP, MBGP
Speaking Routers
Non-Anycast RP
Single RP for
Group(s)
RP
RP might be inconvenient for shared tree
Receiver
Source
Notes: Inconvenient RP: several thousand miles of extra path to get there

## Slide 58: Multicast RP
RP
RP
eBGP, MBGP
Speaking Routers
Anycast RP
Multiple RPs for same group(s)
RP
Can optimize RP placement for locality
MSDP Mesh,
Unique Addresses
Receiver
Source

## Slide 59: Anycast Sinkholes
Problem: Homeless network traffic (e.g. turbo worms, backscatter, etc) can cause problems for core routers to sink; sinkholes help but also don’t want to send traffic across large network to sink
Goal: Want to be able to forward traffic to multiple sinkhole points for analysis
Solution: Use anycast to enable distributed sinkholes throughout a large network
Notes: http://www.nanog.org/mtg-0306/sink.html
http://www.potaroo.net/iepg/march-2003/sink.pdf
http://www.arbornetworks.com/downloads/Sinkhole_Tutorial_June03.pdf

## Slide 60: Anycast Sinkholes
Traffic can be directed to sinkhole via:
  default route
  pieces of unused IP space
  BGP next-hop triggering, ex: for DoS victims
Multiple sinkholes can be deployed using anycast as sinkhole destination address
Very good slides by Greene, McPherson (see resources page for links)

## Slide 61: 6to4 Routers
Problem: Connecting islands of v6 across existing v4 infrastructure involves 6to4 relay routers
Goal: Provide an easy way for end sites to locate relays into the native v6 world
Solution: Use a well-known IPv4 anycast prefix for 6to4 relay routers

## Slide 62: 6to4 Routers
IPv6 Backbone
IPv4 Backbone
6to4
RR
6to4
RR
Advertise
2002::/16 to
v6 backbone
Advertise anycast v4 6to4 prefix
192.88.99.0/24
Advertise
0::/0 internally
Native IPv6 Site
Using 6to4 Prefix
6to4
R
Notes: 6to4 R : 6to4 Router
6to4 RR : 6to4 Relay Router
RFC3056: Connection of IPv6 Domains in IPv4 Clouds
6to4 relay routers announce a route to the v4 prefix
6to4 routers

## Slide 63: TCP-Based Services
Unwise to use anycast for long-term TCP services, due to route changes
Experience shows that routes are generally stable, though
  Especially inter-domain, due to routing protocols
  Equal cost load balancing would cause problems
  But, routers often do flow path caching
Notes: Note the inter-domain vs intra-domain difference here: inter-domain is probably

## Slide 64: TCP-Based Services
Very few knobs to direct traffic in response to server load, as well
“as long as you don't make silly assumptions about client
locality based on "which anycasted server heard it", such that
you give back incoherent answers in hopes that they will be
somehow client-optimal, bgp-anycast isn't even controversial at this point in time.”
- Paul Vixie, 4/03
Notes: http://www.merit.edu/mail.archives/nanog/2003-04/msg00460.html

## Slide 65: Other (Potential) Uses
NTP/Time
Syslog
RADIUS
Kerberos
Single packet request-response UDP protocols are “easy”

## Slide 66: Agenda
What is Anycast?
Deploying IPv4 anycast services
Anycast usage case studies
Advanced Topics
  Multi-homed hosts
  IPv6

## Slide 67: Multi-Homed Hosts
Multi-homing at the host physical interface
Can be used with anycast addressing
Special case: single multi-homed host configured with anycast address
  More appropriately a ‘service’ address
  Server redundancy, no service separation
  Much of the same configuration
  Additional complications with default route
Notes: Default route complications: want to use host based router to control default route, but what if the host-based router goes away?

## Slide 68: IPv6 Anycast
IPv6 Anycast, per RFC3513, is different from “shared-unicast” addressing (what we’re calling anycast)
  3513: Eliminate constraints on routing infrastructure, upper-layer protocols
  Decouple Anycast from any thought about TCP/UDP (and still make it work)
  “Shared Unicast” IPv6 would generally map from v4 experiences
Hagino, Ettikan draft addresses the differences and limitations
Notes: IPv6 Addressing Architecture: RFC3513
Reserved IPv6 Anycast Addresses: RFC2526
DHCPv6: RFC3315
Default Address Selection: RFC3484
http://www.ietf.org/internet-drafts/draft-ietf-ipngwg-ipv6-anycast-analysis-02.txt

## Slide 69: 3513 vs Shared Unicast
Issue | RFC3513 Anycast | Shared Unicast
Identifying anycast dest. | Same address format as unicast | Same address format as unicast
Deterministic packet delivery | None – seq. packets may reach diff. hosts | None – seq. packets may reach diff. hosts
Anycast host addresses | Disallowed; routers only | No restriction
Anycast as source addr. | Disallowed | Required for current operational use
IPsec | Difficult – instability of addressing and routing | Difficult – instability of addressing and routing
Notes: Identifying anycast destinations: both use the same format as unicast
Deterministic packet delivery: None, both rely on routing tables; fragmentation is an issue here
Anycast host addresses: only routers may have RFC3513 anycast addresses

## Slide 70: 3513 vs Shared Unicast
Issue | RFC3513 Anycast | Shared Unicast
Identifying anycast dest. | Same address format as unicast | Same address format as unicast
Deterministic packet delivery | None – seq. packets may reach diff. hosts | None – seq. packets may reach diff. hosts
Anycast host addresses | Disallowed; routers only | No restriction
Anycast as source addr. | Disallowed | Required for current operational use
IPsec | Difficult – instability of addressing and routing | Difficult – instability of addressing and routing
Why?
Questions about how hosts announce routes into domain. Shared-unicast solutions apply.

## Slide 71: 3513 vs Shared Unicast
Issue | RFC3513 Anycast | Shared Unicast
Identifying anycast dest. | Same address format as unicast | Same address format as unicast
Deterministic packet delivery | None – seq. packets may reach diff. hosts | None – seq. packets may reach diff. hosts
Anycast host addresses | Disallowed; routers only | No restriction
Anycast as source addr. | Disallowed | Required for current operational use
IPsec | Difficult – instability of addressing and routing | Difficult – instability of addressing and routing
Why?
Anycast addresses don’t uniquely identify source node. Trying to define most generic solution at IP layer.

## Slide 72: IPv6 Anycast Improvements
Allow hosts to have 3513 Anycast addresses
  Just need to define mechanism(s) for announcing routes into domain
Provide deterministic endpoint with anycast
  Could use routing header specifying non-anycast address as intermediate hop
Anycast address as source address?
  Source address is unique machine address
  Home address option of Anycast address
  Would break semantic equality of source address/home address

## Slide 73: IPv6 Anycast Protocol Issues
3513 and UDP
  DNS, etc. require matching source address as queried destination
  “Use better security and drop the checks”
3513 and TCP
  Connections identified by address/port pair of source/destination
  Provide a means for changing address of connection/initiating new connection?

## Slide 74: IPv6 Anycast General Issues
With emphasis on route aggregation, questions arise about global inter-domain shared-unicast
3513 Anycast specifically: host routes must be carried within aggregation domain encompassing all interfaces of specific Anycast IP

## Slide 75: IPv6 Anycast Addresses
Reserved addresses/ranges (3513)
Subnet-Router Anycast Address
subnet prefix
0000000000000
n bits
128-n bits
Reserved Anycast Addresses
subnet prefix
anycast ID
n bits
7 bits
11111111111
121-n bits
subnet prefix
anycast ID
64 bits
7 bits
111111011..11
57 bits
EUI-64
“Local”
Non-
EUI-64
Notes: The “all zeros” address is reserved for identifying default routers on a subnet (RFC3513)
Reserved anycast address (RFC2526)
Eui-64 has universal/local bit set to ‘0’ to indicate non-global uniqueness in the interface identifier

## Slide 76: Summary
Anycast is relatively simple to deploy in existing networks
Operators are finding new uses for it in different areas
Look for some changes as v6 comes around

## Slide 77: Questions?
Presentation resources: http://www.net.cmu.edu/pres/anycast
Kevin Miller: kcm@cmu.edu
Notes: http://www.pch.net/resources/papers/ipv4-anycast/40

## Slide 78: 6to4 Routers
Native IPv6 Site
Using 6to4 Prefix
6to4
R
Src: 2002:8002:ff1f::1
Dst: 2001:4e8:4:200::1
IPv6
Hosts generate native IPv6 packets

## Slide 79: 6to4 Routers
Native IPv6 Site
Using 6to4 Prefix
6to4
R
6to4 Router encapsulates packet to send over v4 backbone
Note: External v4 address dictates v6 prefix
Src: 2002:8002:ff1f::1
Dst: 2001:4e8:4:200::1
IPv6
Dst: 192.88.99.1
Protocol: 41
IPv4
Src: 128.2.255.31

## Slide 80: 6to4 Routers
6to4
RR
6to4
RR
IPv6 Backbone
Src: 2002:8002:ff1f::1
Dst: 2001:4e8:4:200::1
IPv6
Dst: 192.88.99.1
Protocol: 41
IPv4
Src: 128.2.255.31
Packets delivered to one
anycast relay router
Relay router removes v4
header, forwards into v6

## Slide 81: 6to4 Routers
6to4
RR
6to4
RR
IPv6 Backbone
Src: 2001:4e8:4:200::1
Dst: 2002:8002:ff1f::1
IPv6
Dst: 128.2.255.31
Protocol: 41
IPv4
Src: [RR unique]
Relay routers advertise
2002::/16
Relay router forwards via
6to4 pseudo-interface; v4
address based on v6 prefix

## Slide 82: 6to4 Routers
Native IPv6 Site
Using 6to4 Prefix
6to4
R
6to4 Router removes v4 header; forwards v6
packet locally
Src: 2001:4e8:4:200::1
Dst: 2002:8002:ff1f::1
IPv6
Dst: 128.2.255.31
Protocol: 41
IPv4
Src: [RR unique]

## Slide 83: Identifying Specific Node
F Root Server
  dig hostname.bind @f.root-servers.net chaos txt
K Root Server
  dig id.server @k.root-servers.net chaos txt
.ORG TLD Servers
  dig whoareyou.ultradns.net @tld1.ultradns.net
  dig whoareyou.ultradns.net @tld2.ultradns.net
Notes: dnsmon.ripe.net